Considerations for Over The Air Updates:

- Device Authentication: Device must be authenticated between the Server and the Device. Device authentication would happen during the SetUp phase, and it ideally should have a key ( like Device ID), so that no random device cannot connect with the Main Server and vice-versa.
- The Server would need to have a directory structure to save the updates. Updates could be saved on update-packages/Version-XX
- Networking Policing; Update package needs to be Zipped to reduce the size and can be downloaded off the server. And it should behave like a normal user request and not a high priority request.
  - Package would be transmitted using HTTPS port 443, to avoid opening any new port on Raspberry Pi.
  - HTTP Range requests would be used to retrieve the data from the Server.(The server has to support range requests as well. You could check this by sending a head request. Which requests only for the headers of the response excluding the content. You can check this out by using cURL, a command line tool https://medium.com/@suvanika/multipart-download-and-byte-ranges-b5d6b7577e95.). Using the Content Length and the Accept Range option, we can proceed with partial transfers.(https://developer.mozilla.org/en-US/docs/Web/HTTP/Range_requests)
- Installation of Update: After the package is downloaded, it can be installed on the next reboot.
- Update Package:
  - Package would be zipped and signed by the Server using OpenSSL

  - Upgrade Package should have a folder structure which includes:
    - Update Folder:
      - Script Folder:Should include any scripts which we need to run on the Raspberry Pi to set up some configurations.
      - Config Folder: Includes new configuration settings
      - Executable/Bin folder : Includes new Executables/Binaries and their Dependencies. The Script folders can have the basic scripts which can transfer these executables to the right place.
      - Device Driver folder: Device Driver folder will have all the device drivers which need to be installed in the system. Installation would be done by the scripts in the Script folder.
    - Rollback Folder: Rollback folder will have a set of scripts only. These scripts would revert the system back to the original configuration by using the backups taken before the Update.
    - Metadata	File:
      - Name/Version of the software build
      - All Versions/Device ID formats ( formats can be specific of Wild Carded) where this package can be applied
      - Checksum of the package.
- Update Framework: The next release should have this framework.
  - The framework would be a process which is running on the background on the Raspberry Pi. Based on the Push-Pull design, the process will download the package first.
    - First the Pi will ask the Server is there is a new package for a specific version. Server will respond with a body which has the path of the update package. All of this will happen using HTTPS for secured connection. Package has to be MANUALLY uploaded in TAR format by the Backend Developers on the server.
    - Pi will then confirm if the package can be downloaded using HTTP Range requests. It will start the download in segments if Range is supported , else it will initiate a complete download.
      - If the download terminates due to Network Issues, the service would ping till the network is not back up. Once it is, it will resume the Download process.
    - The framework will use a marker file, which can have the following values:
          - Download , Last Byte, Total Length, Type of Download( Full/Partial )
          - Update, Total Scripts, Completed scripts, Reboot ( Yes/No )
          - Rollback, Total Scripts, Completed Scripts, Reboot (Yes/No)
    - Once the package is downloaded, and based on the update policy the update will occur. Updating the Pi would require:
        - Unzipping the package in a new update/ folder
        - Backing up all the files listed in the executable/bin , configuration/ and drivers/ folder. This can be written in the framework, or can be read from an XML/JSON file which can be created per Update Package. Backup would be created in /update/backup/ folder in the Pi and it would have upto 5 backups, saved based on timestamp ( and Update version if possible). This allows manual retrieval of older configurations in case the new one doesnt work so smoothly.
        - Executing the scripts in the script folder, which would replace the executables, device drivers and update the new configuration files. It would also restart the processes which are affected by these changes. NOTE: IT WOULD NOT REBOOT THE RASPBERRY PI UNLESS ABSOLUTELY REQUIRED.
          Reboot will be done at the end of Update, and not in between.
        - If any error occurs during this time, rollback can be initiated from the backup taken earlier. Rollback can be done using the rollback scripts and the files in the backup folder.
        - If Update is successful, the Rollback script in the Update folder can be copied into the backup directory.
Push-Pull Design:
Push-Pull: Server can send out a Push notification to all Raspberry Pi's that an update is available or Pi can ask the server if an update is available. Once Pi gets a response, it can then send a pull request to the server to get the data. If the Raspberry Pi is turned off before the Update starts but after it downloads the Update, the next update should be done immediately when the Pi restarts.

Server needs to have either an FTP or a service running which provides information of the latest package for a specific version

VPN:
Using VPN for connecting to the server and downloading the Update package reduces network hacking issues like Man-in-the-Middle attacks or spoofing attacks. But using VPN would require tunnelling which would throttle the download speeds further. VPN is not directly tied up with the Update framework and the Update Package can still have some reliability if HTTPS is used.

Guidelines for Updates:
Updating must not under any circumstances break (“brick”) the devices, e.g if the update is interrupted (power loss, network loss, etc.), the system should fall back to a working state . See if its possible to have 2 rootfs. Basically, a reboot should fix the bricked device.
- Updating must be atomic): update succeeded or update failed; nothing in between that could result in a device still “functioning” but with undefined behavior. If there is any failure in the Update, the complete process has to be rolled back.
- Updating must be able to install images/packages that are cryptographically signed, preventing third parties from installing software on your device
- Updating must be able to install updates using an secure communication channel